## Slide 1: Embedded Systems
Anupam Sobti

## Slide 2: What?
An electronic system with a dedicated purpose
Air Conditioner PCB Tutorial With Its Working and Repair - Hackster.io

## Slide 3: What?
Battery Free sensors that float in the wind
Glucoscreen
A wearable ultrasound scanner could detect breast cancer earlier
Amazon Alexa
In-ear EEG

## Slide 4: Why?
Interface between humans and environment
There is no software without hardware and hardware is a rare skill even today
All grand challenges require some hardware:
  Sustainable practices
    Optimal resource usage – energy, water, heat, etc.
    Health
    Food
Augment human intelligence through additional sensing/perception capabilities

## Slide 5: Why should YOU do it?
Build next-gen hardware – drones, robots, but also remotes, fans, air conditioners, cooking stoves, generators!
Build a physical reality for software solutions and vice versa
Sheer lack of stable hardware – broken traffic lights, unrepairable devices, expensive imports!
Upcoming medtech, smart cities!
Jobs: firmware engineer (e.g., Intel, Oculus, Google, Apple), hardware design (medtech, car companies, renewable energy devices, Bosch), etc.
Menti

## Slide 6: Why should you NOT do it?
Chill course hai
Aur kya karein?
Exam nahi hai
... because you will pull your hair out 😄

## Slide 7: How?
Basic electronics – understand power requirements – steady state and transient
Understand Computer Architecture – Every architecture is different offering various specialist use cases
Software – Various programming models are used – embedded C, OS, RTOS, Rust!

## Slide 8: The building blocks
Reliable power source
Power delivery network
Processor
RAM
Persistent Memory
Peripheral Interfaces
Peripherals
Compute
Communication

## Slide 9: Constraints
Battery Life
Form Factor
Cost of failure
Performance requirement

## Slide 10: Some basics
Putting wires together
Hand-holding circuits

## Slide 11: Wires
wires-and-connections.pdf (adafruit.com)
Cables
HF signals
Breadboard | Single core solid wire
HF Signals | Coaxial cables
More current? | Stranded Wires
Wearables | Conductive Threads
Flexible electronics | Copper Tape
Secure your cables | Ties, clips, bolts

## Slide 12: Connectors
wires-and-connections.pdf (adafruit.com)
Barrel Plugs
JST Connectors Japan Solderless Terminals
Power
USB Connectors
Shrinks

## Slide 13: Resistors
From Art of Electronics, 3rd Ed

## Slide 14: Variable Resistors
From Art of Electronics, 3rd Ed

## Slide 15: Capacitors

## Slide 16: Inductors

## Slide 17: Switches

## Slide 18: SMD components

## Slide 19: Course Plan

## Slide 20: Lab Plan
Power Supplies [5]
Toy/Smart Campus Device [15]
Medical Device [15]
RTOS Bot [15]
Each project will have:
- 5 marks for final submission
Rest of the marks = Sum of each lab’s evaluation normalized to 10
To be submitted:
  Sch, brd files
  List of components
  Presentation
  Code
Menti

## Slide 21: Tools
Eagle/KiCAD
Everycircuit
3D printing

## Slide 22: References
Books
Art of Electronics, 3rd Ed. By Paul Horowitz, Winfield Hill
Practical electronics for Inventors by Paul Scherz
https://anupamsobti.notion.site/Embedded-Systems-bf7a3f7e510a444aacaa875ac0c7d83c?pvs=4

## Slide 23
The building blocks
Reliable power source
Power delivery network
Processor
RAM
Persistent Memory
Peripheral Interfaces
Peripherals
Compute
Communication

## Slide 24
Power Supplies
Simple regulator circuit -> Rectifier + Filter
https://everycircuit.com/circuit/5073547604787200
Problems?
Powerline ripple
AC to DC
VDC to VDC
Step-Down
Step-Up
VDC to IDC
Constant Current sources

## Slide 25: Types of power Supplies
Basic idea:
Use a voltage reference with some negative feedback to provide regulation

## Slide 26: Example regulator
https://everycircuit.com/circuit/5202706431737856
Ref: AOE
Overvoltage Crowbar
Overcurrent Protection
Stability

## Slide 27: Thank AIC designers for
7805, 7812, etc.
With a current of upto 1.5A
Ref: PEI

## Slide 28: The assignment
Lesson 1: Read the datasheets uA7800 Series (Rev. J) (sparkfun.com)
  7805 has internal short circuit protection
  Lesson 2: Never trust a software setting. Trust what you see. [mil widths]
  Lesson 3: Never trust a circuit blindly that you find on the internet

## Slide 29: Adjustable regulators
Ref: PEI
Reverse Protection Diode

## Slide 30: Specifications
Output voltage (5V)
Accuracy (10%)
Min and max input voltage (7-12V)
Ripple rejection
Temperature stability
Output impedance
Also note,
  Linear regulators have dropouts (~2V drop between input to output -> Use LDO for lower dropouts, e.g., LM2940)
Ref: PEI
Expected Load = 100mA – 2 A

## Slide 31: Metrics
Ripple
Dropout voltage
Power Supply Rejection Ratio

## Slide 32: Heat Sink
Degrees per watt
Ref: AOE

## Slide 33: Ground plane as heat sink

## Slide 34: Solution Discussion

## Slide 35: Common Applications

## Slide 36: Lower Drop Out
5V -> 3.3V -> 2.5V [Multiple power rails]
Operating from a (declining) battery?
Fractional output-current sample

## Slide 37: The common problem?
Energy dissipation in the pass transistors
  Continuously running currents
  Low efficiency
  High heat generation

## Slide 38: Switchers
The cons:
- Noise
Pros:
- Compact size
- Small capacitor & transistor sizes
- Lower power consumptions
- Saturation or cutoff operation
- No dropouts
- Reliability

## Slide 39: Charge Pumps
Voltage Inverter
Voltage Doubler
Sec 9.6.3 (AOE 3rd ed)

## Slide 40: Switchers with inductors
Oscillation Cycles
Charge the inductor (increase current)
Let the inductor charge the capacitor
[Feedback eliminated for simplicity]

## Slide 41: Buck Converter
https://everycircuit.com/circuit/6494788991582208

## Slide 42: Boost Converter
https://everycircuit.com/circuit/5152487425966080

## Slide 43: Battery Chargers
Constant Current (CC) Constant Voltage (CV) Charging
: CC-CV charging
Typical set point voltage = 4.2 +/- 50mV
1C charging rate = charging current equal to A-hr rating of the cell
Isn’t the battery charged at the end of current limit phase? What’s happening in the CV phase?
The current is reducing and hence the entire 4.2V is from the charge stored and not the drop across ESR (Equivalent Series Resistance)
Ref: TI Note

## Slide 44: LP2951
Other options LP2952 (higher current)
LM317 (cheaper)

## Slide 45: Bonus: Magic Circuit (Joule Thief)
https://everycircuit.com/circuit/5969382857244672

## Slide 46: More common ICs
Ch 17, Practical Electronics for Inventors
- Audio
- Power
- RF
- Medical

## Slide 47: Tool Installation
PlatformIO for AVR controllers

## Slide 48: Make PCBs not War
Reliable power source
Power delivery network
Processor
RAM
Persistent Memory
Peripheral Interfaces
Peripherals
Compute
Communication
Basic tutorial: tech.guitarsite.de/pcb_layout

## Slide 49: What’s a PDN?

## Slide 50: Why is this difficult?
Because a wire is not always a wire. It’s a transmission line..
Impedance discontinuities lead to signal reflections -> Degraded signal quality
https://everycircuit.com/circuit/5698102557933568
Introduction to Signal Integrity for PCB Design - YouTube

## Slide 51: Why does it matter?
Setup and Hold Time Requirements
Signal to noise ratio
When does it not matter?
  Low frequency signals (rise length lR = tRV < 10*trace length)
  Or very short connections [a small PCB is (almost) always a better PCB]

## Slide 52: In action
Avoid cross-overs
Power Delivery Network Analysis (Rev. A) (ti.com)

## Slide 53: Crosstalk
Coupling
  Capacitive: Two conductors induce charge in each other
  Inductive: inducing current in a nearby conductor
  Radiative: Track acting as an antenna
  Common impedance (e.g., ground plane): Return paths interfering with other return paths
Avoiding crosstalk
  Increase distance between wires
  Use differential signaling
  Route traces at right angles (wrt other traces)
  Use termination
  Keep analog/digital return paths separate

## Slide 54: How can you handle it?
Continuous impedance
  Stick to 45 degree routes
    - continuous impedance
    - less chance of inductive coupling
    - better for etching/flex
  Proper terminations into components
Symmetric grounding
  Ground planes
Introduction to Signal Integrity for PCB Design - YouTube

## Slide 55: How can you handle it?
Space Things Out
Use different track widths for signal/power
Use decoupling capacitors
Top 5 Beginner PCB Design Mistakes (and how to fix them) - YouTube

## Slide 56: Let’s see some PCBs!

## Slide 57: Arduino Uno Rev3
Observe:
Voltage Regulation
  Ferrite beads
  Fuses
Decoupling Capacitors
Perpendicular lines in the two planes
Ground Plane
Different mill widths in analog and digital paths
ICSP – In Circuit Serial Programming Interface
USB to Serial conversion with Atmega16U2

## Slide 58: The building blocks
Reliable power source
Power delivery network
Processor
RAM
Persistent Memory
Peripheral Interfaces
Peripherals
Compute
Communication

## Slide 59: Microcontrollers
Embedded into a device that’s certainly not a “computer”
  No disk to boot from
  On-chip compute, memory – both RAM and NVM (Flash) + ADC/DAC + onboard debug and programming interfaces
  Opamp – the universal analog component | mC – the universal digital component
Ref: AOE Ch 15

## Slide 60: Anatomy of a mC

## Slide 61: ATtiny85
[Datasheet]
  8 kB Flash
  256 bytes SRAM
  512 bytes of EEPROM
Watchdog Timer (wake me up)
Internal oscillator/two timer interrupts – do work periodically
All I/O pins interfaces with ADC
I2C, Serial interfaces

## Slide 62: Where’s my clock?
Note: Datasheet is God!
Contains details of all registers to be programmed for a certain function as well

## Slide 63: Attiny LED Blinker
How to Blink an LED with ATtiny85 | ATtiny85 Programming - YouTube
ATTiny Port Manipulation (Part 1): PinMode() and DigitalWrite() : 7 Steps - Instructables

## Slide 64: More complex mCs
AVR (mostly single core)
AC Power Control
Thermal Controller
Remote Controller
STM32 (multi-core)
Drones
Smartwatches/Airpods/Apple TV
PLCs
Medical Monitors/FItbits
Car infotainment systems
Synthesizers and MIDI Controllers
Macbook pro touchbar
Digital Stethoscopes
Notice:
No mention of OS yet
DSP
Audio signal processing, e.g., FFTs
Audio enhancement/noise reduction, etc.

## Slide 65: Common interfaces Switch
Also, pullup/pulldown
Ref: PEI

## Slide 66: Debounce
Hardware Debounce
Software Debounce

## Slide 67: Controlling LEDs

## Slide 68: Analog Input
Direct
Ref: PEI

## Slide 69: High power digital outputs
Typical AVR pin = 40 mA current
Remember to use diodes with inductive components, e.g., relays

## Slide 70: Motors

## Slide 71: Detecting sound levels
Looking for more interfaces?
Refer AOE 15.8

## Slide 72: Capturing Sound
From an audio jack
Microphones

## Slide 73: Generating Sound
Load = 8 ohm piezo speaker

## Slide 74: Amplifying Sound
Linear on-board amplifiers (low gain)
Common ICs – LM386, LM383

## Slide 75: Talking to other devices
Ref:AOE

## Slide 76: One-wire
Reset = 480 mS
0 = 15 mS
1 = 60 mS
Pull Up
Power-less operation

## Slide 77: I2C (TWI)
5/3.3V – 500 bits/s
No parasitic mode – 4 wire interface
Sending Data
Receiving Data

## Slide 78: I2C (TWI)

## Slide 79: Some common I2C devices
RTC
I2C Sensors
I2C ADC (Analog-to-Digital Converters)
I2C DAC (Digital-to-Analog Converters)
I2C GPIO Expanders
I2C Real-Time Clock (RTC) Modules
I2C EEPROM (Electrically Erasable Programmable Read-Only Memory)
I2C OLED Displays
I2C Motor Controllers
I2C Audio Codecs
I2C GPIO Sensors
I2C Expansion Hubs
I2C RTC with NVRAM (Non-Volatile RAM)
I2C Touch Sensors
I2C LED Drivers
I2C Motor Encoders
I2C Gas Sensors

## Slide 80: SPI
Note: Full duplex (upto 80 Mbit/s)

## Slide 81: TTL Serial
Rx, Tx with fixed baud rates
110, 300, 600, 1200, 2400, 4800, 9600, 14400, 19200, 38400, 57600, 115200, 128000, and 256000.
Full Duplex

## Slide 82: MODBUS
An industry standard interface on top of RS485 like signals
  Also implemented over ethernet with TCP/IP stack
  Common in gas/water/energy meters, etc.

## Slide 83: USB
Introduced in 1905
V1 - Low Speed, Full Speed (1. 5 Mbps/12 Mbps) [Differential voltage]
V2 – High speeds (480 Mbps) [Differential voltage based binary encoding]
V3 – Superspeed (4.8 Gbps via shielded twisted pairs) [8b/10b encoding]
  V3.1 – 9.6 Gbps with increased DC power options – 5V, 2A or 12/20V 5A with USB C connector
  Master-slave Star Topology

## Slide 84: Controller Area Network (CAN)
Multidrop km-range bus accommodating upto 30 transceiver nodes
1Mbps for 40m and 10 kbps at 1km (max)
Quiet bus on no data
  Collisions and backoffs

## Slide 85: Programming a Microcontroller

## Slide 86: Programming mC != Programming a computer
There’s only one CPU!
  No task switching unless you make it switch
Plenty of parallel hardware to use
  Use interrupts as much as possible – to (not) wait for all kinds of things!
  Sei() – global interrupt enable
  Cli() – global interrupt disable
Note: The next few slides are Atmega328P specific

## Slide 87: Instruction execution

## Slide 88: Memories
1 kB EEPROM
- parallel r/w
- SPI r/w

## Slide 89: Clock

## Slide 90: Power Management

## Slide 91: I/O
DDRx
PORTx
PINx

## Slide 92: Timer

## Slide 93: ADC Types
Successive Approximation
Example DAC
Sigma-Delta ADC Compared to SAR ADC - Developer Help (microchipdeveloper.com)
How delta-sigma ADCs work, Part 1 (Rev. A) (ti.com)
https://everycircuit.com/circuit/5048641919909888
Delta-Sigma Modulator Basics - YouTube
Delta-Sigma ADC

## Slide 94: ATMega 328P ADC